## Slide 1: Communication System for the AAUSAT-II
Kresten K. Sørensen
kkso02@space.aau.dk
Department of Control Engineering
Aalborg University

## Slide 2: AAUSAT-II Mission Objectives
Education
Communication
(One-way and two-way)
Attitude Determination & Control System
(Detumbling and pointing)
Payload (Gamma Ray Detector)
Deploy extra solar panels
Upload new software for radio amateur use

## Slide 3: AAUSAT-II Overview
MECH - Mechanical structure
OBC – Onboard Computer
CDH – Command Data Handler
COM – Communication
EPS – Electrical Power Supply
P/L – Payload
ADCS – Attitude Determination and Control System
GND – Ground station
MCC – Mission Control Center
Notes: To have all of you to understand how the AAUSAT-II is designed I will start with explaining the subsystems included in this project.
First of all we have the mechanical structure which must fit the demands for a cubesat to be 10 times 10 times 10 cm and a mass at 1 kg.
Next thing is the onboard computer which is the hardware som og the subsystems use for their software to run on.
This is first of all the Command data handler, which takes care of the superior control of the satellite like deciding which subsystems are allowed to run and make sure the satellite is behaving the way it should be. CDH also collects the housekeeping data for all subsystems so they can be send to the earth on a request.
The Payload onboard the satellite is a gamma ray detector which can be used for measuring radiation in space.
The Attitude Determination and Control system shall detumble the satellite and test attitude control of a cubesat using magnetorquers and momentum wheels.
Both P/L and ADCS have a thread running on the OBC
EPS is the Electrical power supply which shall deliver power to the satellite using solar cells.
Finally the Communication system sends and receive data from the ground station and pipes the data directly through to CDH on the CAN bus. COM also sends the basic beacon.
All communication between the subsystems uses the CAN bus
On the earth it is possible to send a flight plan from the Mission COntrol Center. The MCC then sends the data to the ground station which then transmits the telemetri to the satellite, when a pass is present.
The first 6 month of operation AAUSAT-II is used to verify the mission objectives. After that new software will be uploaded and radio amateurs will be able to communicate with it according to telecommands which will be published at that time

## Slide 4: COM System
Purpose
  To create a communication path between the satellite and Earth.
Demands
  Simple, robust design
  Power saving
  Small
  Interface to: CAN, RS232, and Radio

## Slide 5: Block Diagram
Components
  MCU
  Radio
  CAN
  UART
  Modem

## Slide 6: Specifications for COM 1/2
  Radio Frequency: 437.425 MHz (Half duplex)
  6 kHz bandwidth
  Data rates: 1200/2400/4800 bit/sec
  FFSK/MSK-modulation
  Transmitter Power: 0.5 W
  Link budget: (Worst case)
  Downlink margin 6,2 dB
  Uplink margin 20,5 dB
  CAN bus: 125 kbps
Notes: The radio link is half duplex at 437.425 MHz
The CAN Bus is 125 kbps
A mass of 110 gram (10% of 1 kg) Depends on the Antenna the KOM department comes up with
All components on COM uses 3.3 V which gives a power consumption of almost 200 mW when the radio is listening and 300 when receiving, while 2 Watt is used when transmitting.
Data rates at 1200 2400 and 4800 baud can be set by sending a command from MCC which then will be veified before data is transmitted at the selected baudrate. 1200 baud is standard when COM reboots.

## Slide 7: Specifications for COM 2/2
  Mass incl. Antenna: 110g
  Supply voltage: 3.3 V
  Power Consumption
  Listening: 184.8 mW
  Receiving: 283.8 mW
  Transmitting: 2085.6 mW
Notes: The radio link is half duplex at 437.425 MHz
The CAN Bus is 125 kbps
A mass of 110 gram (10% of 1 kg) Depends on the Antenna the KOM department comes up with
All components on COM uses 3.3 V which gives a power consumption of almost 200 mW when the radio is listening and 300 when receiving, while 2 Watt is used when transmitting.
Data rates at 1200 2400 and 4800 baud can be set by sending a command from MCC which then will be veified before data is transmitted at the selected baudrate. 1200 baud is standard when COM reboots.

## Slide 8: Modulation options
  FSK - Frequency Shift Keying
  MSK - Minimum Shift Keying
  GMSK - Gaussian Minimum Shift Keying

## Slide 9: MSK Modulation
Advantages of MSK modem
  Good noise performance compared to FSK
  Easy to use
Disadvantages for MSK modem
  Synchronous interface
Synchronization
  Data must be synchronized to clock
  The modem synchronize automatically on bit level
  Synchronization on byte level must be done in software on the MCU

## Slide 10: Clock Divider
  Adds the possibility of bit rates down to 150 bps by dividing the data clock with 1, 2, 4 or 8
  Gives more than one symbol per bit and makes the signal easier to demodulate.

## Slide 11: Basic Beacon
Basic Beacon format: AAUSATII <data>
  AAUSATII sent as Morse code on FM
    An 800 Hz Morse tone is sent to the radio
    Makes it easier to find the satellite
    Morse tone created with the MCU PWM generator and a low-pass filter
  Data is modulated by the modem
    6 bit battery voltage + 2 bit counter
After low-pass filter

## Slide 12: Protocol
Connectionless AX.25 using UI frames
  Flags used for synchronization
  Header for identification of packets
  Checksum for verification of packet contents
  Connection orientated AX.25 is to difficult to implement considering our demands
  The connection orientation is placed on a higher level on the OBC and GND server.

## Slide 13: Software
Software tasks
  Relay data between GND and CDH
  Send basic beacon
  Collect housekeeping data
Interfaces
  CAN bus
  USART for modem and radio
  UART for GND segment and debugging
Notes: Sende data frem og tilbage mellem GND og CDH.
Grænseflader ud til de andre subsystemer og komponenter

## Slide 14: Software Structure
Interrupt module
  External communication functions
  Time critical functions
Main module
  Internal functions
  Non time critical functions

## Slide 15: Synchronization
Synchronous bit stream without start and stop bits
  Hardware synchronization difficult
  The AX.25 flag is used for synchronization
  Synchronization is done by the ISR
101111001001111110011111100111111001
ISR sync.
CD

## Slide 16: Pictures – Radio prototype

## Slide 17: Pictures – Modem prototype

## Slide 18: Pictures – Modem prototype